Nano Simultaneous RFID reader, ESP32 thing

# 1. Background

I am starting using an ESP32 Thing because I am a little bit tired of the small RAM size and capabilities on the Arduino Uno. The ESP32 provides more ROM, more RAM and looks very interesting.

I was used to the ESP8266 WIFI shield, which runs with AT-commands. But I am extremely surprised about the WIFI-capabilities “out of the box” for the ESP32 Thing. I have used the AdvancedWebServer example as a basis. Easy to connect, extend and adjust. It works MUCH faster and stable than the ESP8266 WIFI shield.

The sketch will connect the ESP32 thing (https://www.sparkfun.com/products/13907) to the local network as a server and constant tries to read RFID tags with a Sparkfun/nano/simultaneousreader ( https://www.sparkfun.com/products/14066) as well as check for client connection.
The detected unique EPC's are stored in an array on the board and can be accessed with the following commands:

epc_cnt : return the number of unique EPC's detected
epc_num : returns the unique EPC numbers comma seperated(EPC NUMBER,)
epc_dct : same as epc_num, but will add to each EPC how often detected (NUMBER:##,)
epc_all : perform get_cnt + epc_dct commands
epc_clr : will remove the EPC's from the array after the next epc_num command
force_epc_clr : will clear all the EPC's from the array immediately

Optional if you had also connected a DS18x20 temperature sensor :
tmp_c : returns temperature in Celsius
tmp_f : returns temperature in Fahrenheit

A similar project I have done on an ESP8266. The challenge with the ESP32 is that this processor has 2 cores/processor. It was much more difficult to get it going. There is a challenge with the onewire-library (see Appendix A) and also with SoftSerial for the ESP32 (see appendix B)

Paul van Haastrecht
December 2018

 THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE DISCLAIMED. IN NO EVENT SHALL THE COPYRIGHT HOLDER OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.
# 2. Hardware connection settings

## 2.1 RFID / NANO reader
Set the onboard switch to HW-UART and connect with lose wires.

RFID reader ESP32 thing (Serial2 is used)
     GND ----------------- GND
     UART TX ---- LS----- 16 (LS = level shifter !!)
     UART RX ------------- 17

The reader is external powered in my case.

WARNING!! WARNING !!WARNING!! WARNING !!WARNING!!

The NANO M6E needs at least 3.7V VCC. It will not work stable on 3.3V.

If you connect to the 5V (USB-V) you MUST use a level shifter for the for RX line from RFID reader to the ESP32. The pins on the ESP-32 can only handle 3V3 signals !!

The RFID RX line, TX / pin 17 from ESP32, actually does not need a level shifter. The 3V3 that is coming from the ESP32 works good for the Nano. HOWEVER for the TX FROM the Nano, did not work well with that level shifter (https://www.sparkfun.com/products/12009)
Apparently the level shifter on the Nano and this level shifter do not work well together. So I made it working with resistors:

        ______ _____
  GND ------| 10K |-----!---- | 5k6 |------ TX from Nano
        -------- ! -------
        !
        pin 16 (ESP32)
## 2.2 Optional temperature sensor (DS18x20 family)

        DS18x20 ESP32 thing
     ____ GND ------------- GND
 .--| 4k7 |-- VCC /red --------- 3V3
 | ‘-----’
 ‘----------- data/yellow ------- 4

You MUST connect a resistor of 4K7 between data and VCC for pull-up.

WARNING!! WARNING !!WARNING!! WARNING !!WARNING!!

The DS18B20 works with VCC between 3 and 5V. It works fine on 3.3V however if connected to 5V you MUST include a level shifter or making a bridge with resistors like below
        ______ _____
  GND ------| 10K |-----!---- | 5k6 |------ data/yellow from DS18x20
        -------- ! -------
        !
        pin 4 (ESP32)

# 3. Software drivers
The sketch is depending on the following libraries and they must have been installed before.

## 3.1 Array handling
https://github.com/janelia-arduino/Vector.git

The array is handled with Vector routines. It handles easily and keeps the code clean.
## 3.2 RFID NANO
https://github.com/sparkfun/SparkFun_Simultaneous_RFID_Tag_Reader_Library

Code for the RFID is based on the examples in the Sparkfun library

Unlike other projects with the RFID NANO reader, I have not connected with SoftSerial but use Serial2 port on the ESP32. See Appendix B for some challenges with softSerial.
## 3.3 Temperature sensor
https://github.com/PaulStoffregen/OneWire

Code for the DS18x20 is based on the DS18x20 example in the onewire library

The ONEWIRE library needs a change. Otherwise it will NOT detect the sensor first time around and/or it will have miss readings. This is documented in Appendix A.

# 4. Program flow
Sketch: ESP32_RFIDSERVER_Vector

Code for the WIFI is based on the ESP32 example AdvancedWebservers sketch. At the top of the sketch a number of options can be set. They are self explaining or documented in the sketch. Following is a list of parameters:
## 4.1 MUST change parameters
for WIFI :
const char mySSID[] = "ssid";
const char myPSK[] = "password";

for RFID/NANO:
RFID_Region

for (optional) TEMPERATURE SENSOR
TEMP_PIN
## 4.2 Optional parameters
for WIFI :
WIFI_PORT 80
MDNS_NAME

for RFID/NANO
RFID_SERIAL_SPEED
RFID_POWER

for console/serial connection
SERIAL

for array size
EPC_COUNT
EPC_ENTRY

for HTML buffer
HTML_BUFFER

There is debug variable: PRMDEBUG : if it will provide sketch flow information.

  0 = no debug information
  1 = tag info found
  2 = 1 + program flow + temperature reading info
  3 = 2 + Nano debug information
## 4.3 program flow
The program flow is straight forward : In setup first initialize and connect to the Nano / RFID reader and clear the array to store the unique EPC. If a onewire-pin was defined (TEMP_PIN) then it will try to connect. After this the ESP32 thing will be connected to the local network. Then it loop wait for an EPC to arrive or client to connect. This client can be a browser.

The command is provided as part of the URL, like 192.168.1.134/epc_cnt or 192.168.1.134?epc_cnt The sketch will act on these parameters from the driver. It will then provide a HTML code page with the answer. In case of 192.168.1.134/get_epc, were it will respond will all the unique EPC’s discovered.

Commands that can be submitted :
epc_cnt : return the number of unique EPC's detected
epc_num : returns the unique EPC numbers comma seperated(EPC NUMBER,)
epc_dct : same as epc_num, but will add to each EPC how often detected (NUMBER:##,)
epc_all : get_cnt + epc_dct commands
epc_clr : will remove the EPC's from the array after the next epc_num command
force_epc_clr : will clear all the EPC's from the array immediately

Optional if you had also connected a DS18x20 temperature sensor :
tmp_c : returns temperature in Celsius
tmp_f : returns temperature in Fahrenheit

Another nice aspect of the AdvandcedWebServer it the MDNS, Multicast DNS . In case your PC supports this (and many do) you do not have to remember the IP address but can connect : http://rfid.local. (the name can be changed in the top of the sketch) . So a command looks like http://rfid.local/epc_cnt. For more detail see https://en.wikipedia.org/wiki/Multicast_DNS or http://www.multicastdns.org/

# 5. sub-routine descriptions
WIFI routine
init_wifi()	: connect, set parameter to check and MDNS

RFID reader
Init_RFID()	: initialize the connection with Nano
setupNano()	: set the parameters in the Nano
Check_EPC()	: read content send by the Nano

Temperature sensor
init_tmp()	: detect sensor of DS18x20 family
read_Temperature()	: read temperature and return Celsius or Fahrenheit

ARRAY handling
Array_Init()	: Initialize array / vector
Array_Cnt()	: return count of EPC in array
Array_Clr()	: remove all entries/clear array
Array_Add()	: Add an EPC to the array, if not there already
Array_Rmv_Entry()	: remove ONE entry from the array

Command handling
handleRoot()	: create return page in case of 192.168.1.134/
handleNotFound()	: create return page in case of invalid command.
epc_clr()	: perform action and create return page in case of /epc_clr
force_epc_clr()	: perform action and create return page in case of /force_epc_clr
epc_cnt()	: perform action and create return page in case of /epc_cnt
epc_num()	: perform action and create return page in case of /epc_num
epc_dct()	: same as epc_num() but add how often detected.
epc_all()	: same as epc_cnt + epc_dct().
get_temp_f()	: perform action in case of /tmp_f
get_temp_c()	: perform action in case of /tmp_c
get_temp()	: read the temperature and create return page in case of temp_f or temp_c

General
serialTrigger()	: display message and wait for Serial input

# Appendix A: changes to ONEWIRE

To get around that the IRAM_ATTR had to be added. It will make sure that this code is stored in RAM and not loaded from ROM. This is important given the microseconds timing that is critical for one-wire. As I use the library on different boards and want to keep one source the following 3 changes can be applied:
in Onewire.h (around line 99)
change
void write_bit(uint8_t v);
uint8_t read_bit(void);
to :
// Write a bit. The bus is always left powered at the end, see
// note in write() about that.
#if defined (ARDUINO_ARCH_ESP32)
void IRAM_ATTR write_bit(uint8_t v);
#else
void write_bit(uint8_t v);
#endif
#if defined (ARDUINO_ARCH_ESP32)
uint8_t IRAM_ATTR read_bit(void);
#else
uint8_t read_bit(void);
#endif
in onewire.cpp (around line 204):
change
void OneWire::write_bit(uint8_t v)
to
#if defined(ARDUINO_ARCH_ESP32)
void IRAM_ATTR OneWire::write_bit(uint8_t v)
#else
void OneWire::write_bit(uint8_t v)
#endif
in onewire.cpp (around line 236)
change
uint8_t OneWire::read_bit(void)
to
#if defined(ARDUINO_ARCH_ESP32)
uint8_t IRAM_ATTR OneWire::read_bit(void)
#else
uint8_t OneWire::read_bit(void)
#endif

# Appendix B. SoftSerial challenge

The ESP32 has 3 serial ports and as such the library does NOT have SoftSerial included by default. Based on the softserial from https://github.com/jdollar/espsoftwareserial, which in turn is based on the Arduino software serial library for the ESP8266 found here https://github.com/plerup/espsoftwareserial

The softserial from Jdollar could not be compile. Once that fixed it hang and paniced constant and was working very unstable on Sparkfun ESP32 Thing. Unfortunately one can not provide issues on the github and the code is now 2 years old.

A number of changes have been applied to make it work:

- Only enableRX after the speed is set to prevent "hang"
- The disable of interrupts has been implemented that it really works during RX and TX
- The timing for bit-banging RX has been adjusted to be more accurate
- The reset for GPIO detected interrupts now works (caused panic)
- Added yield() for low baudrate in the wait during TX (taken from ESP8266)
- Extend default RX-buffer size from 64 to 128 bytes (there is enough RAM)
MAKE SURE TO ADJUST also the following in cores ESP.cpp. It must be set for IRAM_ATTR as it is called during interrupt:

line 103 uint32_t IRAM_ATTR EspClass::getCycleCount() // is called from interrupt !

I have posted my updated version on : https://github.com/paulvha/ESP32/tree/master/softserial

It now works OK-ish, most of the time. But do not expect it to work above 56K (stretch already !!)

It is still better to use any of the three serial interfaces, which are supported by a real uart. The nice aspect is that the pins of each UART/Serial can be assigned to nearly all pins on the ESP32. The pins 9 and 10, default for Serial1, on SparkFun ESP32 Thing are used for flash memory. However as the pins can be assigned for Serial, one can still use Serial1 port bu then on other pins ( e.g. 25 and 26).