Connecting M6E Nano over Bluetooth

# 1.0 Introduction

As part of many projects in my interest area ”where hardware meets software”, sometimes referred to as the world of IOT (Internet of Things), I have now connected my ThingMagic M6E reader to Bluetooth using the RN42 BlueSMiRF Silver from Sparkfun.

While this worked immediately with the Universal Reader Assistant (URA) on Windows-10, I had connection issues with some of the examples in the ThingMagic API. This has been overcome and documented in chapter 6.2’Reading tag on Raspberry Pi / Ubuntu’

Regards,
Paul van Haastrecht

# 2.0 Connect to Bluetooth card under Ubuntu / Raspberry PI

Be superuser : sudo bash

Make sure the bluez package is installed on your system (most of the time it is)
There is a lot of information on the internet how to do that e.g.
sudo apt-get install Bluetooth bluez bluez-tools rfkill
or
sudoapt-get install build-essential libBluetooth-dev
## 2.1 Pair devices
This optional for the Bluetooth card, but many Linux releases require it
### 2.1.1 Raspberry Pi
select Bluetooth icon
select add device
select the Bluetooth card when it appears
select pair
enter pair code ( default 1234)
### 2.1.2 Ubuntu
On the command line type : Bluetoothctl
1. devices (will show up)
2. scan on (if the Bluetooth card is not in the list)
3. agent on
4. pair 00:06:66:DA:06:5B
  (00:06:66:DA:06:5B is my device code,replace it with yours)
  type pair 00 + <TAB>
5. trust 00:06:66:DA:06:5B
  type trust 00 + <TAB>
6. quit

## 2.2 Setup RFCOMM

First scan to get Bluetooth device:

hcitool scan
Scanning ...
00:06:66:DA:06:5B	tmreader

Now get channel
sdptool records 00:06:66:DA:06:5B

Service Name: RNI-SPP
Service RecHandle: 0x10000
Service Class ID List:
  "Serial Port" (0x1101)
Protocol Descriptor List:
  "L2CAP" (0x0100)
  "RFCOMM" (0x0003)
    Channel: 1
Language Base Attr List:
  code_ISO639: 0x656e
  encoding: 0x6a
  base_offset: 0x100

control-c

make RFCOMM

nano /etc/Bluetooth/rfcomm.conf
#
# RFCOMM configuration file.
#

rfcomm0 {
        # Automatically bind the device at startup
        bind no;

        # Bluetooth address of the device
        device 00:06:66:DA:06:5B;

        # RFCOMM channel for the connection
        channel 1;

        # Description of the connection
        comment "Model T Bluetooth";
}

now initiate
rfcomm bind rfcomm0 00:06:66:DA:06:5B 1
will return the prompt and /dev/rfcomm0 is available

OR

rfcomm connect /dev/rfcomm0 00:06:66:DA:06:5B 1
Connected /dev/rfcomm0 to 00:06:66:DA:06:5B on channel 1
Press CTR L-C for hangup

        At this moment /dev/rfcomm0 should exist and can be used to connect
until CNTRL-C is pressed
^C
Disconnected
# 3.0 Connect to Bluetooth card under Windows-10
## 3.1 Pair Bluetooth card
In windows-10 select settings, devices

Make sure that Bluetooth is ON.

Select	+ add Bluetooth of other device

Select	Bluetooth
scanning now starts

Double click on module address when it appears

It will ask for the pair code ( default 1234) and connect

it will then setup the device

Wait until the message that the device setup is complete

## 3.2 Get com-ports to use

In the same screen click on devices and printers
An overview of all known devices and printers will show.
Right-click you PC name
select Bluetooth configuration
select tab com-port
In my case it shows COM3 for outgoing and COM5 for incoming

# 4.0 Terminal connection to Bluetooth card

There are a number of terminal programs available and in essence they all work the same, but have a different UI and more capabilities than needed. We will discuss Putty here as we can use that on both Windows and Linux /Ubuntu, and Minicom from the Raspberry Pi.
## 4.1 Putty on Ubuntu
become superuser : sudo bash

install putty
apt-get update
apt-get install putty

check that Bluetooth card has been bound
ls /dev/rfcomm0
if not : rfcomm bind rfcomm0 00:06:66:DA:06:5B 1
( 00:06:66:DA:06:5B is my device address, replace with yours)

Start Putty
putty <enter>

select serial connection

select device: /dev/rfcomm0

select ‘OPEN’
A new terminal window will open

Go in command mode (depending on Bluetooth card setting it should be done in the first 60 seconds )
$$$	(no enter needed)
now CMD be displayed
D < enter>
*** settings *** are displayed
E <enter>
*** ADVANCED Settings *** are displayed
X < enter>
extended information is displayed
–-- < enter>
END : now you exit command mode

Exit putty
Close the terminal window

If needed unbind to remove device
rfcomm bind rfcomm0 < enter>

## 4.2 Putty on windows

Start Putty
putty <enter>

select serial connection

select device: COM3 (from previous step

select ‘OPEN’
A new terminal window will open

Go in command mode (depending on Bluetooth card setting it should be done in the first 60 seconds )
$$$	(no enter needed)
now CMD be displayed
D < enter>
*** settings *** are displayed
E <enter>
*** ADVANCED Settings *** are displayed
X < enter>
extended information is displayed
–-- < enter>
END : now you exit command mode

Exit putty
Close the terminal window

## 4.3 Minicom from the Raspberry Pi

Become superuser : sudo bash

Install minicom
apt-get update
apt-get install minicom

check that Bluetooth card has been bound
ls /dev/rfcomm0
if not : rfcomm bind rfcomm0 00:06:66:DA:06:5B 1
( 00:06:66:DA:06:5B is my device, replace for yours)

Start minicom
minicom –D /dev/rfcomm0

Go in command mode (depending on Bluetooth card setting it should be done in the first 60 seconds )
$$$	(no enter needed)
now CMD be displayed
D < enter>
*** settings *** are displayed
E <enter>
*** ADVANCED Settings *** are displayed
X < enter>
extended information is displayed
–-- < enter>
END : now you exit command mode

Exit minicom
CTRL – A X
Leave minicom ? YES NO
<enter>

If needed unbind to remove device
rfcomm bind rfcomm0 < enter>

# 5.0 Hardware connection ThingMagic reader and Bluetooth card.

## 5.1 Bluetooth card Hardware

(source : Sparkfun hookup guide)

The Sparkfun Bluetooth comes with 4 different versions : Mate Silver, Mate Gold, SMiRF silver and SMiRF gold.

The Silvers use the RN-42, and the Gold uses an RN-41. The difference between those two modules? Range and transmit power. The RN-41 is a class 1 Bluetooth module, so it can communicate at up to 100 meters, but it also transmits at a higher power (meaning shorter battery life). The RN-42 is class 2, which limits the transmit range to about 10 meters. The software is the same, the command set is the same.

The pin-layout between a MATE and SMiRF differ. The pinout of the Mate matches that of products like the FTDI Basic and the FTDI Cable. It’s a “standardized” pinout for a serial interface and power supply combination. This pinout allows the Mate to be plugged directly into the serial header of Arduino Pro’s and Pro Minis

Mate	SMiRF
1	GND	RTS-O
2	CTS	RX-I
3	VCC	TX-O
4	TX-O	GND
5	RX-O	VCC
6	RTS-O	CTS-0

Do NOT connect RS232 directly to any of these devices. They need TTL level binary signals.

## 5.2 Connecting Reader and Bluetooth module

M6E nano pin layout
1	GND
2	NC
3	VCC	max 5 Volt
4	RX
5	TX
6	NC

Do NOT connect RS232 directly to any of these devices. They are TTL level binary signals.

Depending the Bluetooth board (either the MATE or SMiRF) you need to make the following connection between the pins. Bluetooth board in MATE layout is more straight forward.

M6E nano	Mate	SMiRF
GND	1	1	4
NC	2
VCC	3	3	5
RX	4	4	3
TX	5	5	2
NC	6

# 6.0 Reading tag over Bluetooth

## 6.1 With URA on Windows-10

Make sure have performed the Bluetooth setup on windows

Connect the reader with the Bluetooth device as indicated in chapter and apply the power.

start the universal reader assistant on windows

select the “standard serial connection over Bluetooth COM3 (outgoing)” as detected during setup
of windows

select your region	(EU3 in my case)
select antenna	(M6E nano only has 1)
select connect
wait for the screen to appear
The red light should turn off blinking and green light (connection) on the Bluetooth device should now lid

Depending on your power supply you might need to reduce the read/write power to max 5dbm in the performance tuning menu (if you use USB power only this is advisable for steady performance)

select read
It should ALL work now :-)

## 6.2 Reading tag on Raspberry Pi / Ubuntu

Make sure the Bluetooth setup on Raspberry has been performed
Check that /dev/rfcomm0 exist

Using the standard example of demo
./demo tmr:///dev/rfcomm0

There is an issue when trying to run different examples. This is caused by the fact that once the /dev/rfcomm0 port has been opened it will take some time for the Bluetooth connection to be established.
In TMR_connect() it will open the device and then loop through different baud-rates to detect on what baud-rate the reader is running. (expecting a readable response)
However if the connection is not stable yet, it will have checked all the baud-rates before the connection is established.
This can be overcome by setting a different timeout on the checking than the 100ms (which is default during check on baud-rate)

So right after a successful TMR_create() and BEFORE TMR_connect() do the following (in a C-program or the equivalent in JAVA or C#) to set to 6 seconds timeout :

    // set timeout value for baud-rate detecting on slow connections
    uint32_t val=6000;
    ret = TMR_paramSet(rp, TMR_PARAM_TRANSPORTTIMEOUT, &val);
    checkerr(rp, ret, 1, "setting timeout");

This will cause a delay of maximum 6 seconds before each baud-rate test. If you consider that too long, lower the val and find the right balance for your connection.

# Appendix A.
## Failed to connect to SDP server on FF:FF:FF:00:00:00: No such file or directory
this might help
sdptool is broken in Bluez 5
You need to run the blue tooth daemon in compatibility mode to provide deprecated command line interfaces. You're running Bluez5 and you need some Bluez4 functions. You can do this by editing this file
(Debian based distro)
sudo vim /lib/systemd/system/Bluetooth.service
(RedHat based distro)
sudo vim /usr/lib/systemd/system/Bluetooth.service
and changing this line
ExecStart=/usr/lib/Bluetooth/Bluetoothd
to this
ExecStart=/usr/lib/Bluetooth/Bluetoothd --compat
and then restarting Bluetooth like this
sudo systemctl daemon-reload
sudo systemctl restart Bluetooth
and you'll also have to change permissions on /var/run/sdp
sudo chmod 777 /var/run/sdp