GPIO support Simultaneous RFID tag reader

# 1. Background

Sparkfun has created an Simultaneous RFID tag reader, based on the M6e Nano from Jadak (formally ThingMagic). (https://www.sparkfun.com/products/14066)

Sparkfun has also created a library for the Arduino-like micro-boards which is a scaled down version based on the official Mercury API from Jadak. (https://github.com/sparkfun/SparkFun_Simultaneous_RFID_Tag_Reader_Library)

While this Sparkfun library works stable and good, it is lacking a number of options, including the ability to control the GPIO’s.

These GPIOs are broken out on the board and GPIO01, LV2, LV3 and LV4.

Picture source : https://learn.sparkfun.com/tutorials/simultaneous-rfid-tag-reader-hookup-guide/hardware-overview

This document (and supporting code) provides an enhancement to the Sparkfun library to set and read the GPIO on the Simultaneous RFID tag reader.

August 2019
Paul van Haastrecht

CAUTION CAUTION CAUTION CAUTION CAUTION CAUTION CAUTION CAUTION

From the hardware design manual of the M6e Nano (relevant parts included in Appendix A)

Please be aware and remind yourself that on the Nano GPIO1 and the LV2, LV3, and LV4 pins are 3.3V only. The Sparkfun hook-up guide mentions that GPIO1 is 5V tolerant, but this is not supported by the design guide.

Each line configurable as input or output interface by default it is an input with internal pull-down, with a resistance value of between 20 and 60 kOhms (40 kOhms nominal).

The GPIO pins should connect through 1 kOhm resistors to the module to ensure the input Voltage limits are maintained even if the module is shut off.

Lines configured as inputs must be low whenever the module is turned off and low at the time the module is turned on.

# 2. Software

## 2.1 New library calls

The following new library calls are added :

### 2.1.1 uint8_t setGPIO(uint8_t gpio, bool high);
To set the GPIO output level as HIGH or LOW

### 2.1.2 uint8_t getGPIO(uint8_t gpio, bool *state);
Will return the current GPIO level as HIGH or LOW

### 2.1.3 uint8_t setGPIODirection(uint8_t gpio, bool out, bool value = false);
Will set the GPIO direction as input or output, with starting value.

### 2.1.4 uint8_t getGPIODirection( uint8_t gpio, bool *out);
Will return the current direction of the GPIO

All calls will have a return value of ALL_GOOD if successful else there was an error. The parameters are described in the header file. (nano_gpio.h) and usage in the example1.

## 2.2 New variables
### 2.2.1 GPIO direction
New definition is added for direction :
#define GPIOout 1 // set as output
#define GPIOin 0 // set as input

### 2.2.2 GPIO selection

New definition are added for the GPIO selection (as described on the simultaneous RFID board)
#define GPI01 1 // actually it could read LV1
#define LV2 2
#define LV3 3
#define LV4 4

## 2.3 Package
The solution consists of the following parts:

- nano_gpio.cpp : code to be included into the Sparkfun_UHF_RFID_Reader.cpp
- nano_gpio.h : code to be included into the Sparkfun_UHF_RFID_Reader.h
- nano_gpio_example1.ino : example code of using the gpio extension
- This document describing the installation and changes to be made.

# 3. Installation instructions

Locate the library which is installed on the system where are other libraries for the Arduino IDE are located.

## 3.1 update Sparkfun_UHF_RFID_Reader.cpp

1. Optional : make a copy of the original Sparkfun_UHF_RFID_Reader.cpp
2. Open nano_gpio.cpp AND Sparkfun_UHF_RFID_Reader.cpp with a text editor.
3. Copy the content of nano_gpio.cpp and add this to the END of the Sparkfun_UHF_RFID_Reader.cpp
4. Save the Sparkfun_UHF_RFID_Reader.cpp

## 3.2 update Sparkfun_UHF_RFID_Reader.h

1. Optional : make a copy of the original Sparkfun_UHF_RFID_Reader.h
2. Open nano_gpio.h AND Sparkfun_UHF_RFID_Reader.h with a text editor.
3. Locate the line starting : //Variables in the section Public. (around line 142)
4. Copy the content of nano_gpio.h and add this to the insert BEFORE //Variables the content in Sparkfun_UHF_RFID_Reader.h
5. Save the Sparkfun_UHF_RFID_Reader.h

## 3.3 update keywords.txt

You do not have to change this, but it will enable recognizing and color the new library calls and variables in your sketch. The file is located in library location. While Sparkfun_UHF_RFID_Reader.h and Sparkfun_UHF_RFID_Reader.cpp are in the ‘src’ directory, keywords.txt is located in the parent of that.

1. Optional : make a copy of the original keywords.txt
2. Open keywords.txt with a text editor
3. Add in the section : Methods and Functions (KEYWORD2)
  setGPIO	KEYWORD2
  getGPIO	KEYWORD2
  setGPIODirection	KEYWORD2
  getGPIODirection	KEYWORD2
4. Add in the section : Constants (LITERAL1)
  GPIOout	LITERAL1
  GPIOin	LITERAL1
  GPI01	LITERAL1
  LV2	LITERAL1
  LV3	LITERAL1
  LV4	LITERAL1

CAUTION :
The format is important in order to work correctly. Between the function and the keyword, there MUST only be 1 TAB. So as an example: setGPIO <pressed tab once> KEYWORD2. This is valid for all lines.

NOTE1:
Some text editors have the option to automatically expand TABS to SPACES (e.g. when saving). Make sure your text editor is not doing that as it will fail.

NOTE2:
Changes in the keywords.txt only become valid after a restart of the Arduino IDE.

# 4 Example software

Parts of this code is coming from the original sketches developed by Sparkfun

Open the nano_gpio_example1.ino in the Arduino IDE.

## 4.1. Serial port

By default the sketch is using SoftSerial, but you do not have to. Set NanoSerial to the serial port to use (e.g. softSerial, Serial2 or Serial3 depending on your choice)
Line 40: #define NanoSerial softSerial

## 4.2. Program flow
As part of setup() , setupNano() will be called. This is part of the original sketches designed by Sparkfun. It is followed by setting the region and RFID power. The later is not necessary for the GPIO, but is to be common/standard practice. If you want you can enable debugging, which will show the data exchanged between the reader and the micro. Unless you have understanding of the bytes, do not use it.

As part of loop() there are 3 possible demo routines to show how to use the new calls.

Demo1: will set the gpio in a different directions (input/output) and show how to set and get the information.

Demo2: will use LV2 as output and LV3 as input, to demonstrate that setting LV2 to different levels is read by the LV3. It requires a wire between LV2 and LV3.

Demo3: will blink on the GPIO’s. Just before the code (around line 329) you can define the GPIO to use : BLINKGPIO, the number of blinks: BLINKNUM and the on/off time in mS BLINKDELAY

There is one supporting routine that can be used by all routines : disp_status(uint8_t gpio). This will display the direction of the GPIO and the current level.

# Appendix A : Hardware design guide

GPIO information from the ThingMagic Nano Design Guide (875-0077-01 Rev E)

General Purpose Input/Output (GPIO)

The four GPIO connections, described in the ThingMagic Nano Digital Connector Signal
Definition, may be configured as inputs or outputs using the MercuryAPI. The GPIO pins
should connect through 1 kOhm resistors to the module to ensure the input Voltage limits
are maintained even if the module is shut off.

Module power consumption can be increased by incorrect GPIO configuration. Similarly,
the power consumption of external equipment connected to the GPIOs can also be
adversely affected. The following instructions will yield specification compliant operation.

On power up, the ThingMagic Nano module configures its GPIOs as inputs to avoid
contention from user equipment that may be driving those lines. The input configuration is
a 3.3 volt logic CMOS input and is internally pulled down with a resistance value of
between 20 and 60 kOhms (40 kOhms nominal). Lines configured as inputs must be low
whenever the module is turned off and low at the time the module is turned on.
GPIOs may be reconfigured individually after power up to become outputs. Lines
configured as outputs consume no excess power if the output is left open

The module is specified to operate with DC input levels of between 3.3 and 5.5 V. All
specifications are maintained as long as the total input current is below 1 A. At 1 A, the
internal Voltage regulatorʼs protection circuit allows no more current to be taken in. This
1A current limit will be reached slightly sooner if current is drawn out the Vout line or if the
GPIO lines are supplying current to external circuits.