Nano Simultaneous RFID reader, ESP8266 thing

# 1. Background

I had ordered an esp8266 Thing because I am a little bit tired of the small RAM size and capabilities on the Arduino Uno. The esp8266 provides more ROM, more RAM and looks very interesting.

I was used to the ESP8266 WIFI shield, which runs with AT-commands. But I am extremely surprised about the WIFI-capabilities “out of the box” for the ESP8266 Thing. I have used the AdvancedWebServer example as a basis. Easy to connect, extend and adjust. It works MUCH faster and stable than the ESP8266 WIFI shield.

The project is aimed to read constantly tags in front the the RFID reader, store each unique detected EPC in a local array, that can be handled (read and cleared) remotely. This can be done with a standard browser. Optionally a temperature sensor can be added.

Paul van Haastrecht
November 2018
# 2. Hardware connection settings

Using the ESP8266 Thing (https://www.sparkfun.com/products/13231) and the Nano/ Simultaneous reader https://www.sparkfun.com/products/14066 . Set the onboard switch to HW-UART and connect with lose wires.

Nano	ESP8266 thing

Serial RX-------------- pin 12
Serial TX -------------- pin 13
Serial GND ------------ GND

In my case the Nano is powered by an external power supply. If you want to use the same power as the ESP8266 Thing, connect also a wire between Serial -VCC and +5V on the ESP8266 Thing.

Optional Temperature sensor (DS18x20 family)

 DS18x20 ESP8266 thing

 GND ------------- GND
 5V /red ------------ 5V
 data/yellow ------- pin 4

You MUST connect a resistor of 4K7 between data and +5v for pull-up
# 3. Software drivers
The library for the Sparkfun Nano
https://github.com/sparkfun/SparkFun_Simultaneous_RFID_Tag_Reader_Library

# 4. Program flow
## Sketch: AdvancedWebServer_rfid
At the top of the sketch a number of options can be set. There is debug variable:
PRMDEBUG : if it will provide sketch flow information.

  0 = no debug information
  1 = tag info found
  2 = 1 + program flow + temperature reading info
  3 = 2 + Nano debug information

The others are self explaining or documented in the sketch and there is no need to change any of the code underneath, unless you want to.

The program flow is straight forward : In setup first initialize and connect to the Nano / RFID reader and clear the array to store the unique EPC. If a onewire-pin was defined (TEMP_PIN) then it will try to connect. After this the ESP8266 thing will be connected to the local network. Then it loop wait for an EPC to arrive or client to connect. This client can be a browser.

The command is provided as part of the URL, like 192.168.1.134/get_cnt or 192.168.1.134?get_cnt The sketch will act on these parameters from the driver. It will then provide a HTML code page with the answer. In case of 192.168.1.134/get_epc, were it will respond will all the unique EPC’s discovered.

Commands that can be submitted :
get_cnt : returns the number of unique EPC’s stored
get_epc : returns all the unique EPC’s stored
clr_epc : will enable (or disable) remove the EPC's from the array after the next get_epc command
FORCED_clr_epc: will clear all the EPC's from the array immediately

In case a temperature sensor was detected:
tmp_f: returns temperature in Fahrenheit
tmp_c: returns temperature in Celsius

Another nice aspect of the AdvandcedWebServer it the MDNS, Multicast DNS . In case your PC supports this (and many do) you do not have to remember the IP address but can connect : http://rfid.local. (the name can be changed in the top of the sketch) For more detail see https://en.wikipedia.org/wiki/Multicast_DNS or http://www.multicastdns.org/

# 5. sub-routine descriptions
WIFI routine
init_wifi()	: connect, set parameter to check and MDNS

RFID reader
initialize_RFID()	: initialize the connection with Nano
setupNano()	: set the parameters in the Nano
Check_EPC()	: read content send by the Nano

Temperature sensor
init_tmp()	: detect sensor of DS18x20 family
read_temp()	: read temperature and return Celsius or Fahrenheit

ARRAY handling
init_array()	: clear array
add_ECP_entry()	: add an EPC to the array if not already there
count_entries()	: count the number of EPC’s in the array

Command handling
handleRoot()	: create return page in case of 192.168.1.134/
handleNotFound()	: create return page in case of invalid command.
clr_epc()	: perform action and create return page in case of /clr_epc
forced_clr_epc()	: perform action and create return page in case of /FORCED_clr_epc
count_epc()	: perform action and create return page in case of /count_epc
get_epc()	: perform action and create return page in case of /get_epc
get_temp_f()	: perform action in case of /tmp_f
get_temp_c()	: perform action in case of /tmp_c
get_temp()	: read the temperature and create return page in case of temp_f or temp_c

General
serialTrigger()	: display message and wait for Serial input